## Slide 1: Dynamic Routing Protocols II OSPF
Relates to Lab 4. This module covers link state routing and the Open Shortest Path First (OSPF) routing protocol.

## Slide 2: Distance Vector vs. Link State Routing
With distance vector routing, each node has information only about the next hop:
    Node A: to reach F go to B
    Node B: to reach F go to D
    Node D: to reach F go to E
    Node E: go directly to F
Distance vector routing makes poor routing decisions if directions are not completely correct (e.g., because a node is down).
If parts of the directions incorrect, the routing may be incorrect until the routing algorithms has re-converged.
A
B
C
D
E
F

## Slide 3: Distance Vector vs. Link State Routing
In link state routing, each node has a complete map of the topology
If a node fails, each node can calculate the new route
Difficulty: All nodes need to have a consistent view of the network
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F

## Slide 4: Link State Routing: Properties
Each node requires complete topology information
Link state information must be flooded to all nodes
Guaranteed to converge

## Slide 5: Link State Routing: Basic princples
  1. Each router establishes a relationship (“adjacency”) with its neighbors
  2.Each router generates link state advertisements (LSAs) which are distributed to all routers
      LSA = (router id, state of the link, cost, neighbors of the link)
  3. Each router maintains a database of all received LSAs (topological database or link state database), which describes the network has a graph with weighted edges
  4. Each router uses its link state database to run a shortest path algorithm (Dijikstra’s algorithm) to produce the shortest path to each network

## Slide 6: Operation of a Link State Routing protocol
Received LSAs
IP Routing Table
Dijkstra’s
Algorithm
Link State Database
LSAs are flooded to other interfaces

## Slide 7: Dijkstra’s Shortest Path Algorithm for a Graph
Input: Graph (N,E) with N the set of nodes and E the set of edges
dvw link cost (dvw = infinity if (v,w)  E, dvv = 0)
s source node.
Output: Dn cost of the least-cost path from node s to node n
M = {s};
for each n  M
Dn = dsn;
while (M  all nodes) do
Find w  M for which Dw = min{Dj ; j  M};
Add w to M;
for each n  M
Dn = minw [ Dn, Dw + dwn ];
Update route;
enddo

## Slide 8: OSPF
OSPF = Open Shortest Path First
The OSPF routing protocol is the most important link state routing protocol on the Internet
The complexity of OSPF is significant
History:
  1989: RFC 1131 OSPF Version 1
  1991: RFC1247 OSPF Version 2
  1994: RFC 1583 OSPF Version 2 (revised)
  1997: RFC 2178 OSPF Version 2 (revised)
  1998: RFC 2328 OSPF Version 2 (current version)

## Slide 9: Features of OSPF
Provides authentication of routing messages
Enables load balancing by allowing traffic to be split evenly across routes with equal cost
Type-of-Service routing allows to setup different routes dependent on the TOS field
Supports subnetting
Supports multicasting
Allows hierarchical routing

## Slide 10: Example Network
Router IDs are selected independent of interface addresses
3
4
2
5
1
1
3
2
Link costs are called Metric
Metric is in the range [0 , 216]
Metric can be asymmetric
10.1.1.0 / 24
.1
.2
.2
10.10.10.1
10.1.4.0 / 24
10.1.2.0 / 24
.1
.4
10.1.7.0 / 24
10.1.6.0 / 24
10.1.3.0 / 24
10.1.5.0/24
10.1.8.0 / 24
.3
.3
.5
.2
.3
.5
.5
.4
.4
.6
.6
10.10.10.2
10.10.10.4
10.10.10.6
10.10.10.3
10.10.10.5

## Slide 11: Link State Advertisement (LSA)
The LSA of router 10.10.10.1 is as follows:
Link State ID: 10.10.10.1 = Router ID
Advertising Router: 10.10.10.1 = Router ID
Number of links: 3 = 2 links plus router itself
Description of Link 1: Link ID = 10.1.1.1, Metric = 4
Description of Link 2: Link ID = 10.1.2.1, Metric = 3
Description of Link 3: Link ID = 10.10.10.1, Metric = 0
3
4
2
Each router sends its LSA to all routers in the network (using a method called reliable flooding)

## Slide 12: Network and Link State Database
Each router has a database which contains the LSAs from all other routers

## Slide 13: Link State Database
The collection of all LSAs is called the link-state database
Each router has and identical link-state database
      Useful for debugging: Each router has a complete description of the network
If neighboring routers discover each other for the first time, they will exchange their link-state databases
The link-state databases are synchronized using reliable flooding

## Slide 14: OSPF Packet Format
Destination IP: neighbor’s IP address or 224.0.0.5 (ALLSPFRouters) or 224.0.0.6 (AllDRouters)
TTL: set to 1 (in most cases)
OSPF packets are not carried as UDP payload!
OSPF has its own IP protocol number: 89

## Slide 15: OSPF Packet Format
2: current version is OSPF V2
Message types:
1: Hello (tests reachability)
2: Database description
3: Link Status request
4: Link state update
5: Link state acknowledgement
ID of the Area from which the packet originated
Standard IP checksum taken over entire packet
0: no authentication
1: Cleartext password
2: MD5 checksum
(added to end packet)
Authentication passwd = 1: 64 cleartext password
Authentication passwd = 2: 0x0000 (16 bits)
KeyID (8 bits)
Length of MD5 checksum (8 bits) Nondecreasing sequence number (32 bits)
Prevents replay attacks

## Slide 16: OSPF LSA Format
LSA Header
Link 1
Link 2

## Slide 17: Discovery of Neighbors
Routers multicasts OSPF Hello packets on all OSPF-enabled interfaces.
If two routers share a link, they can become neighbors, and establish an adjacency
After becoming a neighbor, routers exchange their link state databases
Scenario: Router 10.1.10.2 restarts

## Slide 18: Neighbor discovery and database synchronization
Sends empty database description
Scenario: Router 10.1.10.2 restarts
Discovery of adjacency
Sends database description. (description only contains LSA headers)
Database description of 10.1.10.2
Acknowledges receipt of description
After neighbors are discovered the nodes exchange their databases

## Slide 19: Regular LSA exchanges
10.1.10.2 explicitly requests each LSA from 10.1.10.1
10.1.10.1 sends requested LSAs
10.1.10.2 has more recent value for 10.0.1.6 and sends it to 10.1.10.1 (with higher sequence number)

## Slide 20: Routing Data Distribution
LSA-Updates are distributed to all other routers via Reliable Flooding
Example: Flooding of LSA from 10.10.10.1
LSA
LSA
Update database
Update database
ACK
ACK
LSA
LSA
LSA
LSA
ACK
ACK
ACK
ACK
LSA
LSA
LSA
LSA
Update database
Update database
ACK
ACK
ACK
ACK
ACK
ACK
ACK
Update database
10.10.10.1
10.10.10.2
10.10.10.4
10.10.10.6
10.10.10.3
10.10.10.5

## Slide 21: Dissemination of LSA-Update
A router sends and refloods LSA-Updates, whenever the topology or link cost changes. (If a received LSA does not contain new information, the router will not flood the packet)
Exception: Infrequently (every 30 minutes), a router will flood LSAs even if there are not new changes.
Acknowledgements of LSA-updates:
    explicit ACK, or
    implicit via reception of an LSA-Update

## Slide 22: Shortest path routing and link weight selection

## Slide 23: Traffic engineering framework

## Slide 24: OSPF areas (slides by Leon-Garcia & Widjaja)
To improve scalability, AS may be partitioned into areas
  Area is identified by 32-bit Area ID
  Router in area only knows complete topology inside area & limits the flooding of link-state information to area
  Area border routers summarize info from other areas
Each area must be connected to backbone area (0.0.0.0)
  Distributes routing info between areas
Internal router has all links to nets within the same area
Area border router has links to more than one area
Backbone router has links connected to the backbone
Autonomous system boundary (ASB) router has links to another autonomous system.

## Slide 25: OSPF Areas
ASB: 4
ABR: 3, 6, and 8
IR: 1,2,7
BBR: 3,4,5,6,8
Area 0.0.0.1
Area 0.0.0.2
Area 0.0.0.3
R1
R2
R4
R5
R7
N1
N2
N3
N4
N5
N6
N7
To another AS
Area 0.0.0.0
R = router N = network
R8
R3
R6