## Slide 1: PetTrack: Tracking Pet Location and Activity Indoors
Neeraj Alavala2, Haige Chen1, Rishabh Singhal1, Ashutosh Dhekne1
Georgia Institute of Technology
Microsoft
Notes: Good afternoon. My name is Haige Chen. I will present our work, PetTrack: Tracking Pet Location and Activity Indoors. I would like to acknowledge the other authors, Neeraj Alavala who was previously at Georgia Institute of Technology and now at Microsoft, and Rishabh Singhal and Ashutosh Dhekne from Georgia Tech.

## Slide 2
90.5 million
109.6 billion
# of pet-owning households in US
Total pet industry expenditure in US
according to American Pet Product Association
Notes: (Millions) of families in the US have pets in their household. That number has increased during the pandemic to (). Nowadays, with people going back to office and travelling much more frequently, our pet friends are often left at home alone.

## Slide 3
“The Secret Life of Pets”

## Slide 4
Does my cat sleep all day long, or does it play and exercise?

## Slide 5
Did they do something they are not supposed to do?

## Slide 6
Which room does my dog spend the most time in?

## Slide 7
Location
To answer these questions…
???
???
Pose

## Slide 8
Other potential inferences:
Emotional State
Health State
Emergencies

## Slide 9
Problems with pet cameras
Object occlusion
Privacy intrusive
Data intensive
Computationally complex

## Slide 10: PetTrack Overview
Listener
(x, y)
Pose
UWB radio+IMU
Collect and process IMU and UWB data, and post pose and location to cloud
UWB Anchors

## Slide 11: UWB Localization
Why UWB?
Large bandwidth enables precise measurement of time-of-arrival (ToA).
Good at distinguishing multipaths.
Good signal penetration through walls.
Protocol
Pipelined Two-way Ranging
mmWave

## Slide 12: IMU based activity classification
Observation:
  Unique accelerometer signatures of poses
KNN pose classification
TS | 0.02 | 0.04 | 0.06
Ax | 7.85 | 7.68 | 7.70
Ay | 2.47 | 2.55 | 2.45
Az | 1.43 | 1.40 | 1.51
Filter out transitions
Vectorization
Windowed Raw Samples
7.85
2.47
1.43
7.68
2.55
1.40
7.70
……
…
KNN
Pose

## Slide 13: Wearable design
Sensor placement:
  Comfort
  Localization accuracy
  Pose classification accuracy
Hardware considerations
  Form factor
  Power
Animal experimentation approved by IACUC and IRB
Pet-Wearable
Acc
UWB
SDCard
Buzz
RTC Battery

## Slide 14: Listener
Customized TWR message
Pet wearable device is resource restricted.
UWB and accelerometer data should be exported to external device for processing and communication with Cloud

## Slide 15: Implementation

## Slide 16: Results
Localization result at 7 static locations
KNN Pose Classification Confusion Matrix
Classification Accuracy
Static: 98.6%
Freely moving: 88.4%

## Slide 17: Future works
Improve localization accuracy
Recognition of more static poses and motions
More in depth inferences, such as health, and psychology.
Facilitating pet training