## Slide 3: Class Today
Project 1 is out
Read Szeliski 2.1, especially 2.1.5
More about projections
Light, color, biological vision

## Slide 4: Projection: world coordinatesimage coordinates
Camera Center (0, 0, 0)
.
.
.
f
z
y
.
v’
u’
If X = 2, Y = 3, Z = 5, and f = 2 What are U and V?
3
5
-2
?
Notes: Being a little loose about coordinates vs lengths
u and v prime because they are in the same coordinate system as x, y, and z but in later slides u and v will be –u’ and –v’ because they are in their own coordinate system which is mirrored

## Slide 5: Earth as an example

## Slide 6
ISS timelapse. 400 kilometers from Earth

## Slide 7
“The Blue Marble”, taken on December 7, 1972, by the crew of the Apollo 17 spacecraft, at a distance of about 45,000 kilometers
Notes: 45k is very near geostationary orbit (42,164 km)

## Slide 9
Earth from Curiosity Rover, 2014, 160 million kilometers from Earth

## Slide 10
Earth from Curiosity Rover, 2014, 160 million kilometers from Earth

## Slide 11
“Pale Blue Dot” from Voyager 1, February 14, 1990, 6 billion kilometers from Earth
Consider again that dot. That's here. That's home. That's us. On it everyone you love, everyone you know, everyone you ever heard of, every human being who ever was, lived out their lives. The aggregate of our joy and suffering, thousands of confident religions, ideologies, and economic doctrines, every hunter and forager, every hero and coward, every creator and destroyer of civilization, every king and peasant, every young couple in love, every mother and father, hopeful child, inventor and explorer, every teacher of morals, every corrupt politician, every "superstar," every "supreme leader," every saint and sinner in the history of our species lived there – on a mote of dust suspended in a sunbeam.
Carl Sagan

## Slide 12: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u
How do we handle the general case?

## Slide 13: Interlude: why does this matter?

## Slide 14: Relating multiple views

## Slide 16: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u
How do we handle the general case?

## Slide 17: Homogeneous coordinates
Conversion
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 18: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 19: Basic geometry in homogeneous coordinates
Line equation: ax + by + c = 0
Append 1 to pixel coordinate to get homogeneous coordinate
Line given by cross product of two points
Intersection of two lines given by cross product of the lines

## Slide 20: Another problem solved by homogeneous coordinates
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
Intersection of parallel lines
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 21
Slide Credit: Savarese
Projection matrix
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,t
X
x
Notes: We can use homogeneous coordinates to write camera matrix in linear form.

## Slide 22
Object Recognition (CVPR 2006)

## Slide 23
Inserting photographed objects into images (SIGGRAPH 2007)
Original
Created

## Slide 24: Pinhole Camera Model
x: Image Coordinates: (u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)

## Slide 25
K
Slide Credit: Savarese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
Notes: Work through equations for u and v on board

## Slide 26: Remove assumption: known optical center
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 27: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 28: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 29: Oriented and Translated Camera
Ow
iw
kw
jw
t
R
X
x

## Slide 30: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 31: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 32: Allow camera rotation

## Slide 33: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 34: Vanishing Point = Projection from Infinity

## Slide 35: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 36: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 37: Field of View (Zoom, focal length)

## Slide 38
Suppose we have two 3D cubes on the ground facing the viewer, one near, one far.
What would they look like in perspective?
What would they look like in weak perspective?
Photo credit: GazetteLive.co.uk

## Slide 39: Beyond Pinholes: Radial Distortion
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 40: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Homogeneous coordinates
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 41: Reminder: read your book
Lectures have assigned readings
Szeliski 2.1 and especially 2.1.5 cover the geometry of image formation

## Slide 42: Image Formation
Digital Camera
The Eye
Film

## Slide 43: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source
?

## Slide 44: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 45: A photon’s life choices
Absorption
Diffuse Reflection
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 46: A photon’s life choices
Absorption
Diffusion
Specular Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 47: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 48: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 49: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ1
light source
λ2

## Slide 50: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 51: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
t=1
light source
t=n

## Slide 52: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source
(Specular Interreflection)

## Slide 53: Lambertian Reflectance
In computer vision, surfaces are often assumed to be ideal diffuse reflectors with no dependence on viewing direction.

## Slide 54: Digital camera
A digital camera replaces film with a sensor array
  Each cell in the array is light-sensitive diode that converts photons to electrons
  Two common types
    Charge Coupled Device (CCD)
    CMOS
  http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 55: Sensor Array
CMOS sensor

## Slide 56: Sampling and Quantization

## Slide 57: Interlace vs. progressive scan
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 58: Progressive scan
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 59: Interlace
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 60: Rolling Shutter
Notes: http://en.wikipedia.org/wiki/Rolling_shutter
Even DSLRs have this problem.